## Slide 1: Writing Instructions

## Slide 2
The computer and the external equipment are placed in operation by procedures which incorporate loading magnetic tape, making central manual selections , and starting the program. The operator first makes sure that all the equipment which is to be used by the program in store is properly prepared: that is to say that there is paper in the typewriter, that its margins are correctly adjusted, that its switch is set to COMPUTER, and that the power is on. If magnetic tape is to be used, the door of the tape handler is opened.
Is this an instruction?

## Slide 3: The difference between descriptions and instructions
Description
How something is constructed
How it works
Why it is used
Not necessarily how to use a particular machine/tool/device
Instruction
How to operate something with minimum hesitation
Not understand the operation

## Slide 4: Instruction
Selection, arrangement and presentation of information depend on aim and audience
Must enable complete and correct operation
It must provide complete instruction to do so
Audience: the action may be routine and familiar to some but not others
Layout must be convenient and sequential
Correct tone so user feels comfortable carrying out the operations

## Slide 5: Are the instructions complete?
Incomplete instructions can be disastrous
Do not leave out vital information
Ask: what does the reader know and what does s/he need to be told?

## Slide 6: Is this instruction complete?
The reactor jacket may need manual draining of the condensate during warming up.

## Slide 7: Problems
How to drain the condensate manually?
Is it optional to drain it?
How do we know if there is condensate?
How much condensate is tolerable?

## Slide 8: How about this?
Read the level of condensate, shown on the eye-glass. If it is above the 1.5 cm cubed mark, open valve 3 (diagram 2) and allow the condensate to drain away. Close the valve when, steam, not water, comes out.

## Slide 9
The inept beginner and not the bored expert should be the writer’s target when writing instructions.

## Slide 10: What assumptions do you make?
Think about the level of detail required
Put yourself in the reader’s frame of reference
What do you know and what the reader might know about the operation are two different things
Test your instructions by asking someone to follow them with no other aid

## Slide 11: Ambiguity
The domestic plug consists of two parts: the back part which is the main body of the plug and covers up the connections inside, and the front part which supports the three metal projections which fit into the socket.
In order to change the plug firstly unscrew the screw which enables the back part to be removed. Looking inside the plug, i.e. on the back part of the front part, one sees the back part of the projections.

## Slide 12: Sources of ambiguity
Relative words: front, back, top, bottom, hot, cold
  “Select a suitable amount of choke for weather conditions and temperature of the engine.”

## Slide 13: Sources of ambiguity
Words with double meaning
  “Set the temperature control to 20°C and run up the transmitter to normal working.”
  “Check undercarriage locking pin. If bent, replace.”
  “Check reading of thermocouple read-out.”

## Slide 14: Sources of ambiguity
Unusual words or unusual uses of familiar words
  “Two or three wires can now be seen to be stemming from inside a wider tube.”
  “After the program has been entered, the software pilot lights are displayed.”

## Slide 15: Sources of ambiguity
Ambiguous grammar
  The screws on the connection must be loosened to enable the cables to be entered.
  Cooking spaghetti: Put three pints of water on the cooker—drop in spaghetti—stir.

## Slide 16: Check your instructions
Accurate and complete and contain enough information for the user to do the job
Comprehensible to every member of the likely audience, and contain no ambiguities of usage or grammar
In correct and rigorous sequence, with no gaps and loops
Safe and readable

## Slide 17: Check your instructions
Find a friend unfamiliar with the operation to test your instructions and go over them with a sense of humour to ensure they fulfill their purpose

## Slide 18: Correct sequence for faultless operation
In order to be functional and successful instructions should follow exactly the order of the various operations required
  Adjust flow through valve 4.23. this requires a check on temperature, and before adjusting the valve, opening briefly the cylinder drain valve.
Here the operator has to remember three steps and do them in reverse order
It is difficult to read and could lead to a mistake

## Slide 19: Correct sequence for faultless operation
Open the cylinder and drain the valve for five seconds.
Is the temperature between 180 and 220 degree celsius? If not, adjust control 4.27 and pause until the temperature is within limits.
Adjust the flow through valve 4.23 until the meter reads between 4350 and 4450 litres/minute.

## Slide 20: Dangerous instructions
Start the vacuum pump from the START button local to the pump
Before starting, check that cooling water flow and return valves are open (CW1 and CW2) and that the trade water valve is open.
The trade water control valve is pre-set and should not be adjusted.

## Slide 21: Which invites correct operation?
Run in 900lbs of Chemical 1 into reactor until scale reading is 1100lbs.
Repeat 11, 12, and 13.
  Or
Run in 900 lbs of Chemical 1 into reactor
Note the scale reading. If it is less than 1800 lbs, repeat 11, 12 and 13. If it is 1800 lbs. or over, continue to 15.

## Slide 22: The layout of instructions
Although removing power from the equipment is primarily a maintenance responsibility, the operator can ensure that the system is inoperative by taking several steps. Firstly the reader motor is turned off from the console, and then the magnetic tape is unloaded by pressing the REWIND UNLOAD button whereupon the tape reverses to a point where the tape can be removed. The tape leader is clamped, the door closed, and the power OFF switch pressed. Finally, the following switches are pressed in turn: typewriter OFF switch, MASTER CLEAR switch, and the computer OFF switch, and the computer and peripherals are now shut down.

## Slide 23
Removing power from equipment
Turn off the reader motor at the console READER switch
Press the REWIND UNLOAD button to unload the magnetic tape (the tape will reverse to a point where it can be removed)
Clamp the tape leader
Close the door
Press the power OFF switch
Press the typewriter OFF switch
Press the MASTER CLEAR switch
Press the computer OFF switch

## Slide 24: Group exercise
Write instructions for riding a motorcyle.

## Slide 25: Sequence of sections
Best arranged in sequence of sentences identified clearly by headings
Headings should identify the purpose of the action, not just name the equipment/step
Subheadings help readers divide a long sequence into smaller stages, and provide a resting place

## Slide 26: Sequence of sections
Introductory explanations
  Provide over-view: purpose of actions, what will be achieved and why the result is useful. Short sentences.
Tools required
  Enables advanced selection of tools if special tools are required
Materials required
  List unusual material that need to be found in advance
Definitions
  Provide definitions for words that may not be understood
  Ever-day words with special or restricted meanings

## Slide 27: Sequence of sections
Warnings
  Writer of instructions is reponsible for safety
  Choose a sequence that is safe and provide warning appropriately
  For a particularly dangerous process warning should be given in both the preliminary section and just before the instruction to which it relates
  Use capitals, bold-type to make warnings stand out
  Distinction between different levels of risk
    Note, Caution, Warning, Danger
  Use simple and clear commands/imperatives
  Provide brief explanation: e.g. Keep naked flame away from evacuator pump: ammonia gas is explosive.

## Slide 28: Numbering instructions
Use a simple system
Continuous numbering that goes across sections is best
See p. 211 for example

## Slide 29: Style for operating instructions
Classwork:
Read the remaining sections of the chapter (p. 210-215)
In groups of four make powerpoint slides to present the main points of these sections to the class